…

### Description of Each Level

Operation Level

This level is displayed when you turn the power ON. You can move to the protect level, initial setting level and adjustment level from this level. Normally, select this level during operation. During operation, the process value, set point and manipulated variable can be monitored, and the alarm value and upper- and lower-limit alarms can be monitored and modified.

### Adjustment Level

To select this level, press the LEVEL key once for less than one second. This level is for entering set values and offset values for control. This level contains parameters for setting the set values, AT (auto-tuning), communications writing enable/disable, hysteresis, multi-SP, input shift values, heater burnout alarm (HBA) and PID constants.

Initial Setting Level

To select this level, press the LEVEL key for at least three seconds in the operation level. This level is for specifying the input type, selecting the control method, control period, setting direct/reverse action and alarm type. To return to the operation level, press the LEVEL key for at least one second.

Protect Level

To select this level, simultaneously press the LEVEL and MODE keys for at least one second. This level is to prevent unwanted or accidental modification of parameters. Protected levels will not be displayed, and so the parameters in that level cannot be modified.

# STEP 1 (Initial Settings)

To select this level, press the LEVEL key for at least three seconds in the operation level., using the MODE key to scroll through the parameters.

Set values for each of the displayed parameters can be changed by using the UP and DOWN keys

### CHANGES TO SETTINGS

## INPUT TYPE = 1

TEMPERATURE UNIT = C

SET POINT UPPER LIMIT = 120.0

## SET POINT LOWER LIMIT = 0.0

PID ON/OFF = Pid

STANDARD CONTROL = Stnd

SELF TUNING = On

CONTROL PERIOD = 2

DIR/REV OPERATION = or-r

ALARM 1 TYPE = 3

# STEP 2 (Operational Settings)

To return to the operation level, press the LEVEL key for at least one second,

use the MODE key to scroll through the operation parameters.

Set values for each of the displayed parameters can be changed by using the UP and DOWN keys

#### CHANGES TO SETTINGS

## SET POINT = As Required (0.0 – 120.0)

RUN/STOP (r-S) = rUn

ALARM 1 (Al-1) = -10

# STEP 3 (Adjustment & Autotuning)

To select this level, press the LEVEL key once for less than one second and use the MODE key to scroll through the adjustment parameters. Locate the AUTOTUNE parameter (At) and set to on using the UP and DOWN keys

NOTE:- On returning to the Operation level the Display will flash until the AUTOTUNE procedure has been completed (AUTOTUNING may take some time)

# STEP 4 (Protection)

To select this level, simultaneously press the LEVEL and MODE keys for at least one second and use the MODE key to scroll through the operation parameters. Set values for each of the displayed parameters can be changed by using the UP and DOWN keys

#### CHANGES TO SETTINGS

## OPERATION/ADJUSTMENT PROTECTION = 2

INITIAL SETTING/COMMUNICATION PROTECTION = 2

SETTING CHANGE PROTECTION 1  = oFF